Raspberry Pi Pico Edukit3 Inspired Robot

After receiving my Raspberry Pi Pico & experimenting for a while I decided it old be useful to put it together in a more practical project.
To do this I decided to rebuild my 1st robot which was based around the CamJam Edukit 3 kit with a few minor tweaks & substitutions.

The Edukit 3 consists of :
1	Motor controller board for raspberry pi (all models including the original model B)
2	DC Motors
2	Red Wheels
1	Ball Castor
1	Small Beadboard
1	AA Battery box (4 AA batteries)
1	Ultrasonic Distance sensor (SR04)
1	Line following sensor

+ various resistors, jumper cables & a sturdy box that many owners use as the chassis for the robot until they can make something different.

Tweaks & Substitutions

- 3d printed a suitable chassis - https://www.thingiverse.com/thing:1113796
- replaced the edukit3 motor controller board with a SN754410 H-Brigde IC, the CamJam board can be used but connecting it to the Pico would require an adaptor for the connector, (Neil Lambeth @neilredrobtics has a pico to Pi adaptor board that would be perfect for this if you want to use it https://www.tindie.com/products/redrobotics/pico-2-pi-adapter-board.
- Added a 2nd ½ size breadboard, this fits in the raspberry Pi mounting of the chassis perfectly & is ideal for mounting the Pico & SN754410 driver IC.
- Replaced the 5v SR04 sensor from the Edukit with a more modern 3.3v version so that I did not need the extra resistors to protect the Inputs to the Pico.

Because the Pico is very low current & has an onboard PUS that can accept 2V-5.5V it means that the whole robot can run from the AA batteries in the battery holder, a raspberry Pi requires an additional USB power bank), use rechargeable batteries as fresh alkalines would be slightly over voltage.

Current software

motor.py provides a simple robot class to provide forward, backward, left & right movement.

SR04Pio.py makes use of the Pico’s PIO feature to interface with the ultrasonic sensor, distance is continually scanned & the last result made available as a class variable which can simply be read as needed using the IRQ feature of PIO means the next value can be read every time it is available avoiding out of data if the FIFO is not read fast enough.

Edukt3.py is the basic robot code,

It has IR control – using an RC6 format remote control (mine was obtained from the late lamented Maplins)

The mode can be selected using Radio(Remote Control) Video (line follow) & Music (Avoidance) buttons on the remote.

Direction arrows control the direction with OK being stop
the Power button stops all movement until another mode is selected, further enhancements may need to be made to shut down all the PIO activity to reduce power consumption.